|  | D445-1 | D445-2 DP/PN | D455-2 DP/PN |
| --- | --- | --- | --- |
| Performance index (compared to D445-1, approx.) (*) | 1 | 1.3 | 3 |
| Minimum servo / interpolator cycle | 0,5 ms | 0.25 ms / 0.5 ms (**) | 0.25 ms / 0.5 ms (**) |
| Maximum number of axes (Motion Control axes) | 64 | 64 | 128 |
| Max. number of axes for integrated drive control (servo / vector / V/f) | 6 / 4 / 8 (alternatively) (drive control based on the CU320, Firmware Version V2.x) | 6 / 6 / 12 (alternatively) (drive control based on the CU320-2, Firmware Version V4.x) | 6 / 6 / 12 (alternatively) (drive control based on the CU320-2, Firmware Version V4.x) |
| PROFIBUS interfaces | 2 | 2 | 2 |
| PROFINET interfaces | 1 interface with 4 ports (optionally via CBE30) | 1 interface with 3 ports (onboard) | 1 interface with 3 ports (onboard) |
| Ethernet interfaces | 2 | 2 | 2 |
| DRIVE-CLiQ interfaces | 6 | 6 | 6 |
| Option slot | Yes (TB30 / CBE30) | Yes (TB30) | Yes (TB30) |
| Number of DI | 8 DI | 12 DI | 12 DI |
| Number of DI/DO | 8 DI/DO: max. 6 measuring inputs max. 8 output cams | 16 DI/DO: max. 16 measuring inputs max. 8 output cams | 16 DI/DO: max. 16 measuring inputs max. 8 output cams |
| Output cams, reproducibility | 125 µs | 10 µs | 10 µs |
| Output cams, resolution | 125 µs | 1 µs | 1 µs |
| RAM | 96 Mbyte (< V4.2 SP1: 70 Mbyte) | 128 Mbytes | 256 Mbytes |
| Remanent memory | 364 Kbytes | 512 Kbytes | 512 Kbytes |
| Buffering of remanent user data (retain variable) | up to 5 days: via SuperCap > 5 days: via battery | unlimmited buffering (maintainance-free) | unlimmited buffering (maintainance-free) |
| Buffering real-time clock | up to 5 days: via SuperCap > 5 days: via battery | up to 4 days: via SuperCap > 4 days: via battery | up to 4 days: via SuperCap > 4 days: via battery |

(*) PLC and Motion Control performance, exact value is application-dependent
(**) 0.25 ms for I/Os and hydraulic drives on the PROFINET

. Ordering information

| Order Numbers | Designation | Version/Remark |
| --- | --- | --- |
| 6AU1400-2PA21-0AA0 | 1 Gbyte CompactFlash Card (CF) for SIMOTION D4x5-2 With SIMOTION Kernel/Firmware and SINAMICS S120 drive software; current software release; can be pre-licensed via Z-options Remark: Only for SIMOTION D445-2 DP/PN and D455-2 DP/PN | V4.2 SP1 (SINAMICS V4.4 HF4) |
| 6AU1445-2AD00-0AA0 | Control Unit D445-2 DP/PN programmable Motion-Control controller; HIGH performance; interfaces: 12 DI, 16 DI/DO, 6 DRIVE-CLiQ, 2 PROFIBUS, 3 PROFINET ports, 2 Ethernet, 2 USB, 1 option slot; incl. dual fan / battery module and battery | Requires SCOUT V4.2 SP1 or later |
| 6AU1455-2AD00-0AA0 | Control Unit D455-2 DP/PN programmable Motion-Control controller; ULTRA-HIGH performance; interfaces: 12 DI, 16 DI/DO, 6 DRIVE-CLiQ, 2 PROFIBUS, 3 PROFINET ports, 2 Ethernet, 2 USB; 1 option slot; incl. dual fan / battery module and battery | Requires SCOUT V4.2 SP1 or later |
| 6AU1432-2AA00-0AA0 | Controller Extension CX32-2 Converter control module; for scaling the number of drive axes with SIMOTION D4x5-2; interfaces: 6 DI, 4 DI/DO, 4 DRIVE-CLiQ | Requires SCOUT V4.2 SP1 or later |
| Licenses | The existing licenses (POS, GEAR, CAM, TControl, ...) can also be used for SIMOTION D4x5-2. The MultiAxes Package D445/D445-1 can also be used for D445-2 DP/PN and D455-2 DP/PN. That means D445-2 DP/PN and D455-2 DP/PN use the same MultiAxis Package! |  |
| MultiAxes Bundles | For SIMOTION D4x5-2, MultiAxes Bundles won't be offered anymore (packages consisting: Control Unit, CompactFlash card + MultiAxes Package license). Please order instead: For SIMOTION D445-2 DP/PN: Control Unit D445-2 DP/PN: 6AU1445-2AD00-0AA0 CompactFlash card with MultiAxes Package license: 6AU1400-2PA21-0AA0 -Z M44 For SIMOTION D455-2 DP/PN: Control Unit D455-2 DP/PN: 6AU1455-2AD00-0AA0 CompactFlash card with MultiAxes Package license: 6AU1400-2PA21-0AA0 -Z M44 |  |